## Slide 1: A-CORD (Analytics for CORD)

## Slide 2: Goal
Analyze
(Analytics Engine)
Enable programmable observability and closed loop control based on analytics
Programmable Observability
Control
Examples:
Resource scaling & load balancing
SDN Flow Rerouting (Traffic Engineering)
Blacklisting Subscriber Traffic
Examples:
Fault correlation and Root cause analysis
Fault prediction, Resource utilization prediction
Anomaly Detection
E2E SLA Violation Detection
Examples:
Observe packet ‘inter-arrival-time’ of signaling traffic for a given time window and notify results
Activate smart vProbe and Observe S1-U traffic for a target subscribers for a given time and notify events
Notes: Programmable Observability using which the level of observability from the underlying systems can be programmed as needed.

## Slide 3: A-CORD
ROADM
(Core)
PON
OLT MACs
BBUs (Multi-RATs)
Enterprise
Metro Ethernet
VNF
VNF
VNF
VNF
Configuration
TSDB
Programmable Observability
Collection
Data Storage
Monitoring-as-a-Service
Service Controller (XOS)
CORD Orchestration
Platform
Security Analytic Apps
Diagnostic
Analytic Apps
Real-time
Analytic Apps
Program & Observe
Control
Observed Data
Control Decision
Analytics Engines
Programmable
Probes
Change Observability
Notes: A-CORD consists of 4 key elements.
The first one is Programmable probes that provides deep observability of what is happening inside the network. These probes will be available at each and every element inside CORD, both at hardware elements such as disaggregated access devices, compute/storage servers, fabric whitebox switches, ROADMs...etc and they could be at virtual or software elements such as virtualized network functions running inside VMs & Containers on the compute servers. That way these probes will be available at both infrastructure level as well as at service level such that it enables e2e observability. More importantly these probes will provide the flexibility to control what to observe and when to observe instead of always being enabled and observing everything.
The second key element inside A-CORD is logically centralized monitoring-as-a-service. The key functionality of this element is to abstract and provide a unified interface to program and observe the underlying probes thereby decoupling the higher layers from underlying targets. This is a highly scalable and multi-tenant subsystem.
Next up in the stack is analytics applications and engines that digest the observed data and perform real-time and batch analytics over that data by applying the context specific intelligence to understand the complete state of the system. These applications and engines can be simple open source versions or could be sophisticated closed proprietary ones. (open and closed source)
The outcome of these analytics engines could be either to dynamically adjust the observability or derive what actions need to be taken to optimize the state of the system and feed them to CORD orchestration layer.
So the last part of A-CORD is where the CORD orchestration subsystem executes those control decisions on the network thereby closing the control loop

## Slide 4: A-CORD
Programmable probes: Infrastructure and Service level probes
  Hardware building blocks: Access devices (OLT), Switches, Servers, ROADMs
  Software building blocks: vBBU, Service VNFs running in VMs/Containers
Monitoring-as-a-Service
  Decouples analytics engines from underlying targets
  Unified interface to program and observe hardware and software probes
  Scalable Time Series Data Store for traces of observed data and analysis results
Analytics Engines
  Performs real-time and batch analytic computing of collected data
  Can be simple open source versions or sophisticated closed proprietary ones
  Examples: Root cause analysis/Diagnostics, Resource optimization, Resource capacity predictions, Fault prediction
Closed loop control
  Examples: SDN enabled devices - Flow rerouting, Scaling and load balancing of services running in VMs/Containers

## Slide 5: Monitoring-as-a-Service
Scalable, Multi-tenant Service
Leverages Micro-services Architecture
Decouples applications from probes
Collect once, consume by many apps
Applications can be data sources too
New analytics & probes can be easily brought-in
Data Collection Service
Probe Configuration Service
Data Storage Service
Data Delivery Services
TSDB
Data Storage
Monitoring-as-a-Service
Inventory
Plugins
Probe Configuration
Data Collection
Plugins
Data Delivery
Query
Pub/Sub
Observe
Program
Analytic Engines
Program
Query
Service Controller (XOS)
Notification
*Data = Data Collected from Probes
Notes: Data Collection Service
  Extendable framework to collect data from physical and software probes in CORD
Probe Configuration Service
  Extendable framework to enable probe configuration in a multi-vendor environment
  Provides unified programmatic interfaces to configure the probes
  Probe inventory maintains the mapping between probe and collection points
Data Storage Service
  Scalable database framework that supports multiple back ends.
Data Delivery Services
  Caters to both big data type analytics engines and real-time analytics engines by supporting Query and Publish/Subscribe interfaces

## Slide 6: Monitoring-as-a-Service: Data Collection Service
Event Parser Plugins
Distributed Message Bus
Supports both push and pull based data retrieval
Data Collection
Data Parser
Plugins
VNFs
Service VNFs
VNFs
Compute, Storage
VNFs
Access, Fabric, Core
Data Parser
Plugins
Data Parser
Plugins
Message Bus (Kafka…etc)
PUB/SUB
Query
Data Delivery
TSDB
Data Storage
PULL/PUSH
Notifications to subscribed applications over Kafka, UDP
Notes: Data/Event Parser Plugins
  Target/Probe specific plugins that retrieve and parse the data from probes
  Dynamically loaded when the target/VNF needs to be monitored
  Supports both push and pull based data retrieval mechanisms
  Exports the parsed data for consumption over a distributed message bus.
    Data Storage service consumes the data from message bus and stores them in time series data base (TSDB).
    Data Delivery service consumes the data from message bus and delivers it to all subscribed applications.

## Slide 7: Monitoring-as-a-Service: Proof-of-Concept
To begin with, Monitoring-as-a-Service is implemented using:
  Open Stack Ceilometer*
  sFlow
Monitoring-as-a-Service
Ceilometer-as-a-Service
sFlow-as-a-Service
PULL using REST/
PUSH using RabbitMQ
sFlow over UDP
VNFs
Service VNFs
VNFs
vProbes
VNFs
Compute, Storage
VNFs
Access, Fabric, Core
*Leverages Ceilometer as a starting point, but we have decoupled Ceilometer from OpenStack and we have deconstructed Ceilometer into sub-systems that can be enhanced and replaced as necessary.

## Slide 8: Programmable Probes
Monitoring-as-
a-Service
Monitoring Agents on the Target
  Exposes APIs to program the underlying probes
  Pushes the probe data into data collection modules or Exposes APIs to pull the probe data
Collection Plugins in Monitoring Service
  Probe/Target Specific collector plugin that receive raw data and normalizes data before pushing to higher layers
Probe Config Plugins in Monitoring Service
  Probe/Target Specific configuration plugin that translates higher level monitoring intents to target/probe specific configuration commands
Target
Probes
(n)
Probes
(n)
Data Storage
Probe Config Plugin
Probe Configuration
Data Collection
Data Parser Plugins
TSDB
Data Delivery
Config
API
Pull
API
Monitoring Agent
PUSH
Logic
Pull
Push
Program
Notes:   Monitoring Agents on the Target
    Exposes APIs to program the underlying probes
    Pushes the probe data into data collection modules or Exposes APIs to pull the probe data
  Collection Plugins in Monitoring Service
    Probe/Target Specific collector plugin that receive raw data and normalizes data before pushing to higher layers
  Probe Config Plugins in Monitoring Service
    Probe/Target Specific configuration plugin that translates higher level monitoring intents to target/probe specific configuration commands
Essential components in programmable probes:
The first one is Monitoring agents that reside on the target that front-end the probes by exposing the necessary APIs to program the underlying probes. Similarly it has APIs to retrieve the data on demand and has logic to push the probe data as and when they are available to an external system.
Service/Target specific event parser plugins in the Monitoring-as-a-Service that interfaces towards Monitoring agent and parses the received probe data.
Service/Target specific probe configuration plugins in the Monitoring-as-a-Service that translates the higher level observability commands into target/probe specific configuration commands.

## Slide 9: Programmable Probes: OLT Access Devices
OLT
GPON
ASIC
Monitoring Agent
OpenFlow Agent
OpenFlow
NetConf
vOLT Control App
Data Collection
vOLT_Control_
Plugin
TSDB
Data Delivery
ONOS_Plugin
OLT_
Plugin
vOLT Control App Events
- vOLT.active.subscribers
- vOLT.subscriber.connected
- vOLT.subscriber.disconnected
- TBD
SoC Level Probes
- OLT.optical.interface.power.level
- TBD
OpenFlow Probes/Metrics
- switch.port.receive.packets
- switch.port.transmit.packets
- switch.port.receive.bytes
- switch.port.transmit.bytes
- switch.port.receive.drops
- switch.port.transmit.drops
- switch.port.receive.frame_error
- switch.port.receive.overrun_error
- switch.port.receive.crc_error
- switch.port.collision.count
- switch.table.active.entries
- switch.table.lookup.packets
- switch.table.matched.packets
Infrastructure Metrics
- instance.cpu
- instance.vcpu
- instance.memory.usage
- instance.network.incoming.bytes.rate
- instance.network.outgoing.bytes.rate
- instance.disk.usage
- instance.create
- instance.delete
- hardware.ipmi.node.cpu_util
- hardware.ipmi.node.mem_util
- hardware.ipmi.node.io_util
OLT HW
Abstraction
VM
Monitoring-
as-a-
Service
Programmable Probes

## Slide 10: Programmable Probes: Fabric Switches
Fabric
Whitebox
sFlow Agent
OpenFlow Agent
OpenFlow
Fabric Control App
Fabric_Control_ Plugin
ONOS_
Plugin
sFlow_
Collector
Data Collection
TSDB
Data Delivery
SoC Agent
SoC_
Plugin
BRCM ASIC
OpenFlow Probes/Metrics
- switch.port.receive.packets
- switch.port.transmit.packets
- switch.port.receive.bytes
- switch.port.transmit.bytes
- switch.port.receive.drops
- switch.port.transmit.drops
- switch.port.receive.frame_error
- switch.port.receive.overrun_error
- switch.port.receive.crc_error
- switch.port.collision.count
- switch.table.active.entries
- switch.table.lookup.packets
- switch.table.matched.packets
Fabric Control App Events
- TBD
sFlow
- Packet Samples
OF-DPA
SoC Level Probes
- TBD
Monitoring-
as-a-
Service
Programmable Probes

## Slide 11: Programmable Probes: Service VNFs
VNF(s)
Monitoring Agent
Infra_Plugin
VNF_Plugin
Servers
Monitoring Agent
Data Collection
TSDB
Data Delivery
Compute Hardware
Network
Storage
Virtualization Layer
Virtual Compute
Virtual
Storage
Virtual
Network
Infrastructure Metrics
- instance.cpu
- instance.vcpu
- instance.memory.usage
- instance.network.incoming.bytes.rate
- instance.network.outgoing.bytes.rate
- instance.disk.usage
- instance.create
- instance.delete
- hardware.ipmi.node.cpu_util
- hardware.ipmi.node.mem_util
- hardware.ipmi.node.io_util
Service Level Events
vSG
- vsg.dns.cache.size
- TBD
vMME
- TBD
vBBU
- vbbu.power.level
- TBD
OpenFlow
OVSDB
VTN
VTN_Plugin
ONOS_
Plugin
OpenFlow Probes/Metrics
- From Virtual Network Switches
Virtual Tenant Networking App Events
- TBD
Monitoring-
as-a-
Service
Programmable Probes

## Slide 12: Analytic Engines
Analytic Engines
A-CORD decouples analytics engines from underlying targets
Performs real-time and batch analytic computing on collected data
Diverse Analytics
  Real-time Analytics
  Diagnostics
  Predictive Analytics…etc
Simple open source analytics and sophisticated closed proprietary analytics engines
Predictive Analytics
Real-time Analytics
Diagnostics
Monitoring-as-a-Service
Programmable Probes
Probes
(n)
Probes
Request for Probe Data
Program Probe
Observe
Notify
Notes: A-CORD decouples analytics engines from underlying targets
  Analytics Engines submits request for probe data
  Monitoring-as-a-Service translates the request into Identification of targets to collect the probe data and program
Analytics Engines perform real-time and batch analytic computing of collected data
Diverse Analytics
  Real-time Analytics
    Examples: Anomaly Detection, Congestion Detection, Resource overload Detection…etc.
  Diagnostics
    Examples: Fault isolation & RCA, Customer Care
  Predictive Analytics
    Examples: Resource Capacity Planning, Fault Prediction
Some simple open source analytics will be built and bundled as part of A-CORD releases while allowing more sophisticated 3rd party analytics engines to be plugged in.

## Slide 13: Analytic Engines - Interfaces
Monitoring-
as-a-
Service
Data Storage
Programmable Observability
TSDB
PUB/SUB
Query
Data Delivery
REST Query API
Notifications over Kafka, UDP
Request for Probe Data over REST
Authorization
Analytic Engines
Predictive Analytics
Real-time Analytics
Diagnostics
Interfaces exposed by Monitoring-as-a-Service
  Observability API
    Analytics engines may use this interface to request for any probe data with specified parameters
  Query API
    To retrieve the collected data
  Data Notification
    To notify the collected data at real-time to analytics engines
Authentication to control access to probe data
Observability API

## Slide 14: Closed Loop Control
“Closed Loop Control” is key in making networks Autonomic
Analytics engines derive control decisions
CORD Orchestration layer is responsible for execution of control decision
Dynamic change of observability
  For deriving more intelligent control decisions, Analytics engines may dynamically change the level of observability (Broader vs Deeper) during the decision process
Monitoring-as-a-Service
(Programmable Observability)
CORD Orchestration Platform
Analytic Engines
CORD
(Programmable Probes)
Observe
Execute
Control Decision
Analyze Observed Data
Derive
Control Decision
Change Observability
Program
Notes: “Closed Loop Control” is key in making networks Autonomic (Self-managed, Self-protected) and in SLA fulfillment
“Closed Loop Control” means Continuously observing and analyzing probe data to derive control decisions to optimize the state of the system and then executing those control decisions
Once analytics engines digest the collected data, the outcome of those analytics would lead to either in change of observability for more deeper insights or in deriving a set of control decisions
For deriving more intelligent control decisions, Analytics engines may dynamically change the level of observability (Broader vs Deeper) during the decision process
CORD Orchestration layer (XOS+ONOS) is responsible for execution of control decisions

## Slide 15: Closed Loop Control - Interfaces
Analytic engines would invoke, depending on the control decision, the APIs exposed by corresponding services in CORD. Examples:
  Access Service Controller
    Exposes REST API to control Access devices
  Network Controller
    Exposes REST or gRPC API to program the intents or flows in the network
  Service Specific Controller
    Exposes service specific REST APIs
CORD orchestration layer also provides TOSCA-based interface to be used at design time to onboard the services dynamically
Analytic Engines
XOS
Controller
Access
Access Controller
Controller
ONOS
Network Controller
Controller
vSG/vCDN/
vEPC…etc.
Service Controller
Observed Data
REST API
Examples:
- Adjust OLT power levels
- Disconnect Subscriber
REST/gRPC API
Examples:
- Intent API
- Flow Objective API
- SR Traffic Engineering API
REST API
Examples:
- Scale Up/Down
- Set Uplink bandwidth
- Blacklist Subscriber
Execute
Control Decision

## Slide 16: Closed Loop Control – SON in Mobile CORD
RRH
Mobile edge
vBBU
SON
Agent
vBBU
SON
Agent
Centralized Core
SON
Application
SON
Portal
M-CORD Platform
XOS + ONOS + Service Controllers
Monitroing-as-a-Service
Observed Data
Control Decision
Observed Data Examples:
Power level
CQI
Control Decision Examples:
Adjust power
Load balance among cells
Instantiate new vBBU
SON ( Self Organizing Network) Application
  Closed loop control with RAN ‘Observe & RAN Control Action’
  SON application collects and control RAN through M-CORD platform
Notes:   Observed Data examples: power level, CQI (Channel Quality Indicator)
  Control Decision examples: Adjust power, Load balance among existing cells and optimize performance for UEs, Instantiate a new BBU (that is a new cell for more capacity)

## Slide 17: Closed Loop Control – Service Scaling in M-CORD
M-CORD Platform
Analytics applications
Mobile edge
vEPC
EPC
VMs
EPC
VMs
Back
-haul
Centralized Core
Service
VMs
Central
Core
Slice
XOS + ONOS + Service Controllers
Monitroing-as-a-Service
Observed Data
Control Decision
Observed Data Examples:
Inter arrival time
Jitter
Control Decision Examples:
Instantiate new SGW-C, SGW-D, PGW-C, PGW-D
Monitor service QoE & QoS and trigger new EPC service VMs to handle increased traffic when needed

## Slide 18: Closed Loop Control – Other Use Cases
Congestion detection in Fabric & SDN based Traffic Engineering
Autonomic Anomaly Detection and Mitigation
Adaptive Chaining of Services based on QoE

## Slide 19: Smart Virtual Probe
Embedded programs that can perform data aggregation and simple analytics to reduce data volumes and enable low latency control loops.
Smart virtual probes also helps to monitor VM to VM traffic where traditional probes cannot monitor inside the server
An application can dynamically download different programs depending on the state of the system
Smart virtual probes can be deployed in physical devices (like SmartNICs, P4 enabled devices…etc.) or in virtual environment (inside VM/Container)
Examples:
  Instantiate a smart virtual probe inside SmartNIC card that can monitor flow features (such as inter packet arrival times) from set of subscribers for a specified duration and send events whenever they match a DDoS attack pattern
  Instantiate a smart virtual probe in P4 enabled devices that record the latency at each hop and compute and report the end-to-end latency at the final hop
  Instantiate a custom DPI probe in the data path and mirror the traffic from specified subscribers to the DPI probe that can perform application specific analytics and report the results-For application specific SLA/QoS (-e.g Ensure Pokemon GO connection doesn't go down!)
Notes: Smart Virtual Probe is an embedded program in the data plane that can perform data aggregation and simple analytics to reduce data volumes and enable low latency control loops.
Smart virtual probes are required to monitor VM to VM traffic where traditional probes cannot monitor inside the server
An application can dynamically download and program different smart virtual probes depending on the state of the system
Smart virtual probes can be deployed in physical devices (like SmartNICs, P4 devices…etc.) or in virtual environment (inside VM/Container).
Examples:
  Instantiate a smart virtual probe inside SmartNIC card that can monitor flow features (such as inter packet arrival times) from set of subscribers for a specified duration and send events whenever they match a DDoS attack pattern
  Instantiate a smart virtual probe in P4 enabled devices that record the latency at each hop and compute and report the end-to-end latency at the final hop
  Instantiate a custom DPI probe in the data path and mirror the traffic from specified subscribers to the DPI probe that can perform application specific analytics and report the results-For application specific SLA/QoS (-e.g Ensure Pokemon GO connection doesn't go down!)

## Slide 20: Smart Virtual Probes - SmartNIC
Compute Node
Smart virtual probes can be computationally intensive
Applications configure chain of smart virtual probes and download to the kernel using eBPF C programs or P4 programs
These programs can then be pushed to the SmartNIC
Openflow custom action to identify flows to send to virtual probes
E.g. application specific SLA/QoS analytics (e.g Ensure Pokemon GO connection doesn't go down!)
SmartNIC
Deliver to Host
Update Stats
OVS Datapath
(SmartNIC)
OVS Userspace
(ovs-vswitchd)
OVS Datapath
(Kernel)
VM
SmartNIC Accelerates the Kernel Path
User Space
Kernel Space
Monitoring-as-a-Service
CORD Orchestration
Analytics Engines
OpenFlow
Activate pre-defined vProbe for selective flows
Activate vProbe for given flows
VM
vProbeApp
NetDev
Deploy vProbe
Vrobe Results
Smart vProbe
Smart vProbe
Notes: Smart virtual probes can be computationally intensive
For performance, low level processes (e.g packet inter arrival times, connection tracking etc) can be downloaded to the kernel using standardized stateful eBPF C programs or stateless P4 programs
These programs can then be pushed to the SmartNIC
This model (acceleration as a service for the kernel data path) ensures vendor independence and performance

## Slide 21: Smart Virtual Probes – Programming Model
QoS Check s1
Active Test Monitor
SLA Check s1
Basic DPI
eBPF IR
P4
C
Basic DPI
SLA Check
s2
QoS Check
SLA Check
s1
DDoS Check
Deliver to Host
Update Stats
Dynamic Match/Action
vProbe Primitives
Mirror Packets
INT Endpoint
User Configures Chain of Primitives in vProbe
Openflow custom action can be used to identify which flows to send to vProbe
Example Configuration
OVS Datapath
Hooks to SmartNIC
(optional)
Kernel/
User Space
Smart
vProbe
Deploy vProbes to Target

## Slide 22: Smart Virtual Probes – P4 Enabled Switches
Custom P4 programs recording latencies at each hop in data path
This can then be used to identify a faulty device within the switch fabric
Leaf Switch
Virtual Switch
Leaf Switch
Leaf Switch
Spine Switch
Spine Switch
Virtual Switch
Server
Server
Monitoring-as-a-Service
P4
P4
P4
P4
P4
P4
P4
CORD Orchestration
Deploy P4 based vProbes
vProbe
Results
Payload
Latency
Header
Payload
Latency
Header
Latency
Payload
Latency
Header
Latency
Latency
Latency
Notes: INT: In-band Telemetry is a tool for root cause analysis across a switch fabric.
Once a problem is detected within a network and the problem is identified by vProbes as not being application/server/flow specific then INT can be used
Custom P4 headers Containing timestamps can be used for root cause analysis across a switch fabric
Each Device in data path adds a header containing a timestamp
This can then be used to identify a faulty device within the switch fabric
Using P4 allows the same logic to be used at endpoints and in switch fabric

## Slide 23: Smart Virtual Probes – Compute Intensive Programs
Deploy compute intensive virtual probes such as DPI in the user space VM/Container
Mirror the traffic from specified flows (match condition)
VNFs
Service VNFs
VNFs
vProbes
Fabric or vSwitch
Access
Monitoring-as-a-Service
CORD Orchestration
Analytics Engines
Notify data from existing probes
1
Analytics Engines require more insights of traffic
Activate vProbe
2
3
Instantiate vProbe
4
Deploy vProbe in VM/Container
5
Mirror traffic to vProbe
6
Program Network
Perform Analytics
7
8
Report events
Notify data from vProbes
9
Notes: A-CORD provides flexibility to dynamically deploy compute intensive virtual probes such as DPI in the user space VM/Container and mirror the traffic from specified flows (match condition) to such probes
Monitoring-as-a-Service uses services of CORD orchestration layer to deploy this type of virtual probes
  XOS instantiate the custom virtual probe inside VM/Container on compute cluster
  ONOS programs the network to mirror selective traffic to the probes

## Slide 24: Active Testing
Passive Monitoring vs Active Testing
  Passive Monitoring is where various probes on the network targets collect useful data and will be reported when requested.
  Active testing involves dynamically injecting synthetic traffic into the network or towards a target service and monitor the flow of that traffic and report the results to analytics systems.
Example objectives of Active Testing
  Reproduce & diagnose the customer care issues and E2E network connectivity issues
  To analyze the round-trip performance, latency between devices or services
  To verify E2E SLAs are being met
A-CORD enables deployment of software-based Active Testing agents as programmable probes inside CORD.

## Slide 25: Active Testing in A-CORD
Active Test Controller
Active Test Agents
Active Test Collector
OLT/
vBBU
vRouter
vRouter
Active Test Analytics
Active Test Agent
(Source)
Active Test Agent
(Sink)
Enable Source & Sink Probes
Deploy & Activate Probes
Report Results
Notify Results
1
2
2
3
4
5
Active Test Controller & Collector
Monitoring-as-a-Service
Notes: Analytics Engines submit request to instantiate active test agents along with parameters such as time windows, intervals, measurements to perform…etc.(in this example, test is to validate fabric throughput across racks)
Monitoring-as-a-Service identifies the placement of active test agents and deploy and instantiate them inside VM or Container using CORD orchestration layer (XOS+ONOS) and provide communication between the agents
  In this example, a Source and Sink active test agents are instantiated
Active Test agents start the test traffic between them and monitor the flows at both Source and Sink agents
During the test, Active Test agents collect the various measurements of the flows and report them to Monitoring-as-a-Service when the test is completed
Monitoring-as-a-Service notifies the results to Analytics Engines

## Slide 26: Active Testing: CORD Use Cases
Fabric Connectivity, Throughput Validation & Congestion detection
E2E Subscriber Internet Connectivity and SLA validation
Certification of New CORD Services
Monitor Video Quality of Experience

## Slide 27: Current Implementation
Proof-of-Concept
  Implementation of Monitoring-as-a-Service using openstack ceilometer and sflow based data collection, storage and delivery mechanisms in CORD development (cloudlab & devstack) environment
  Integration with existing probes in CORD (Compute & Hypervisor, ONOS SDN controller, vSG service VNF)
  Implementation of open source Service aware Auto-scaling analytics application and Residential Subscriber diagnostics portal on top of A-CORD
  Integration of A-CORD platform with 3rd party analytics applications

## Slide 28: A-CORD Collaborators & Interest
ON.Lab
AT&T
Ericsson
Verizon
Google
Broadcom
Viavi
Accton
Netronome
Cavium
Airhop

## Slide 29: Long-term Roadmap (1/3)
Programmable Probes
  Hardware
    OLT GPON
      Implement OpenFlow metrics
      Define and implement ASIC level Metrics (power_levels…etc)
      Expose metrics of ‘OLT Hardware Abstraction’ VM
    Fabric whitebox
      Implement sFlow agent
    ROADM
      Implement OpenFlow Metrics
      Implement sFlow agent
Ensure each hardware element implements minimum set of programmable probes before they are introduced in CORD

## Slide 30: Long-term Roadmap (2/3)
Programmable Probes
  Software
    vSG VNF
      Define and implement subscriber traffic events
      Define and implement subscriber service events
    vOLT ONOS Application
      Define and implement subscriber connection events
    vRouter ONOS Applications
      Define and implement subscriber internet connectivity events
    VTN and Fabric controller ONOS Applications
      Define and implement metrics
    Active Testing
      Active test agents for fabric connectivity
    Virtual Probes
      “Inter packet arrival” & “Jitter” virtual probes to be pushed to OVS kernel data path or SmartNICs
Ensure each service VNF implements minimum set of programmable probes before they are introduced in R/M/E CORD

## Slide 31: Long-term Roadmap (3/3)
Monitoring-as-a-Service
  Deployment of Monitoring-as-a-Service using Ceilometer and sFlow in CORD POD
  Replace Ceilometer components with OpenStack Monasca based API and data storage subsystems to improve query API performance
  Explore Ceilometer Gnocchi framework
  Load balancing framework for Ceilometer event parser plug-in subsystem
  Containerize publish/subscribe delivery service
  Framework for programmability of probes
  Integration of Monitoring Service with new probes
  Framework for smart vProbes and Active Testing
Analytics Applications
  Visualization (Dashboard)
  Fault correlation and Root cause analysis for service VNF faults
  Fabric network connectivity and throughput validation using Active Testing Probes
  End-to-End SLA violation detection using Active Testing Probes
  DDoS detection and mitigation
  For more use cases of closed control loops, refer to R/M/E-CORD slides

## Slide 32: A-CORD Plan in 2016
Programmable Probes
Compute Servers
Hypervisors
vSG VNF
Monitoring-as-a-Service
Decouple from Openstack to be deployable in CORD POD architecture
Automation of deployment process
Framework for enabling/disabling services & resources to be monitored
Analytics
Enhanced Visualization/Dashboard
Basic Features
Programmable Probes
Integration of BroadView agent with ONL (Open Networking Linux) on Trident2/Tomahawk chipsets
Monitoring-as-a-Service
BroadView configuration and parser plugins
Connectivity from fabric switches to monitoring service
Connectivity from analytics application to monitoring service
Analytics (BroadView Analytics)
Micro burst detection using BST
Live Traffic Triggered Trace Profile
E2E latency computation for live traffic
Analytics driven dynamic path optimization
Adaption to A-CORD
BroadView Analytics
Programmable Probes
Sample open source active test agents for validating fabric connectivity & throughput
Monitoring-as-a-Service
XOS Service Controller w/ LMAP Service controller & collector
Connectivity from active test agents to monitoring service
Connectivity from analytics application to monitoring service
Analytics
Virtual Truck Roll
Monitoring Service performance KPI
Active Test Analytics
ON.Lab, Ericsson
ON.Lab, Broadcom, ONL
ON.Lab, Viavi
Programmable Probes
Integration of sFlow agent with ONL (Open Networking Linux)
Monitoring-as-a-Service
XOS Service Controller for sFlow collector
Connectivity from fabric switches to sFlow collector
Connectivity from analytics application to monitoring service
Analytics
Elephant Flow Collision detection and mitigation
sFlow Analytics
ON.Lab, Accton

## Slide 33: A-CORD & BroadView Analytics (1)
PON
OLT MACs
BBUs (Multi-RATs)
Enterprise
Metro Ethernet
VNF
VNF
VNF
VNF
VNF
VNF
ROADM
(Core)
CORD
VNF
VNF
CORD Orchestration
Platform
BroadView Collector Plugin
BroadView Config Plugin
CORD
Monitoring-as-a-Service
BroadView Analytics
Control
Program & Observe

## Slide 34: A-CORD & BroadView Analytics (2)
Fabric
Whitebox
Switch
SDK
BRCM ASIC
(Trident2, Tomahawk)
OCP Bare Metal Hardware
BroadView Agent
Monitoring-as-a-Service
A-CORD Probe Configuration
A-CORD Data Collector
BroadView Config Module
A-CORD Plugin
BroadView Collector
REST
RabbitMQ
CORD Network Diagnostics
JSON RPC
REST
REST
REST
1
2
3
4
Diagnostics application pulls the observed data over REST interface and displays the LAG resolution of a given switch
enable_fabric_lag_resolution_diagnostics <pcap_trace>
broadview_packet_trace_enable
broadview_packet_trace_lag_resolution <pcap_trace>
BroadView agent replays the packet trace and periodically send the lag_resolution reports over JSON RPC. BroadView Collector (https://github.com/openstack/broadview-collector) plugin directs the reports to A-CORD central collector.

## Slide 35: M-CORD Analytics Roadmap
Programmable Probes
vBBU VNFs
Monitoring-as-a-Service
vBBU configuration and parser plugins
Analytics
Airhop eSON analytics applications
eSON
Programmable Probes
vEPC VNFs
Monitoring-as-a-Service
Configuration and parser plugins
Analytics
vEPC service scaling
vEPC Optimizations
Programmable Probes
Smart virtual probes for jitter computation, packet inter arrival time computation
Monitoring-as-a-Service
Framework for smart vProbes
Analytics
Visualization
SmartNICs?

## Slide 36: A-CORD: Other Exploratory Areas & Inputs from Service Providers
AT&T, Verizon
  Framework for Smart Virtual Probes/Dynamic Analytics using Smart NICs and P4 enabled devices that perform simple aggregation and simple analytics on the target itself to enable low latency control loops close to the targets and reduce the amount of probe data sent to higher layers
Google
  Focus more on OAM analytics
    Release Qualification (Release Impact Analytics) by aggregating & correlating probe data using build/release tags
  Framework for Hierarchical/Cross-site Analytics
  Emphasizing to have a common Probe Definition language (OpenConfig/Yang…etc)
  Tenant Quota enforcement such that one tenant doesn’t swamp TSDB
  Explore OpenConfig for vendor neutral framework to discover the telemetry capabilities of network elements, to program targets/probes and specifying desired data & its format.

## Slide 37: Summary
A-CORD enables programmable observability and closed loop control based on analytics
  Fully exploits SDN & NFV
  Fully exploits Micro-Services
  Monitoring-as-a-Service provides programmable observability
  Analytics Engines derive intelligent control decisions from the collected data
  XOS+ONOS executes the control decisions on the CORD system