## Slide 1: G.fast in VOLTHA
Addition of Second Access Technology (Reintroduction and conceptual overview)
4/12/2018
Phillip Herron – ADTRAN

## Slide 2: How To Extend VOLTHA
Desire to add additional access technologies to VOLTHA
Architecture proposals to ensure
  Principles of CORD / ONOS are honored
  Operator use case requirements are met

## Slide 3: VOLTHA Rooted In Abstraction
ONOS SDN Controller
Create abstraction of devices of various access technologies and vendors to a common OpenFlow switch model
OLTs
OpenFlow
VOLTHA
Physical representation
ONU/ONTs

## Slide 4: VOLTHA Rooted In Abstraction
ONOS SDN Controller
VOLTHA
Create abstraction of devices of various access technologies and vendors to a common OpenFlow switch model
OpenFlow
Logical representation

## Slide 5: VOLTHA Rooted In Abstraction
ONOS SDN Controller
VOLTHA
When adding G.fast DPU topology, VOLTHA will abstract G.fast in the same fashion as PON
Architecture should allow
  P2P ethernet-fed DPUs
  PON-fed DPUs
  Other copper technologies are not precluded with second access technology pattern
    G.hn
    Fixed Wireless
    5G
OLT
ONU / ONT
DPU
CPE
OpenFlow

## Slide 6: VOLTHA Rooted In Abstraction
ONOS SDN Controller
VOLTHA abstraction for G.fast
  DPUs are OpenFlow switches
  DPU uplink port is logical NB port on OF switch
  CPE ports are dynamic logical SB ports on OpenFlow switches
VOLTHA abstraction for PON
  OLTs are OpenFlow switches
  OLT uplink ports are logical NB ports on OF switch
  ONT UNI ports are dynamic logical SB ports on OpenFlow switches

## Slide 7: G.fast-Based OpenFlow Switch
Example deployments
Core
Access
OLT switch port per ONT UNI
DPU switch port per CPE
PON
P2P Ethernet-fed DPU
PON-fed DPU

## Slide 8: Cascaded OF Switches in VOLTHA
VOLTHA
OLT
ONU / ONT
DPU
CPE
ONOS
RG
The DPU is initially unreachable.
OLT is pre-provisioned and enabled.
OLT DA creates logical switch.
ONU must be activated.

## Slide 9: Cascaded OF Switches in VOLTHA
VOLTHA
OLT
ONU / ONT
DPU
CPE
ONOS
RG
ONU activates.
Port added / port up.
EAPOL exception flow pushed down.
Default / bootstrap profile provisioned.
DPU reachable.

## Slide 10: Cascaded OF Switches in VOLTHA
VOLTHA
OLT
ONU / ONT
DPU
CPE
ONOS
RG
DPU authenticates.
DHCP / subscriber flows pushed down.
Controller / orchestrator snoops auth or DHCP.
Calls preprovision_dpu which launches DPU DA.
DPU DA creates logical switch and connects to DPU.
DPU DA initializes the DPU.

## Slide 11: Cascaded OF Switches in VOLTHA
VOLTHA
OLT
ONU / ONT
DPU
CPE
ONOS
RG
CPE trains up.
Port added / port up.
Default / bootstrap profile provisioned.
EAPOL exception flow pushed down.
RG reachable.

## Slide 12: Cascaded OF Switches in VOLTHA
VOLTHA
OLT
ONU / ONT
DPU
CPE
ONOS
RG
RG authenticates.
DHCP / subscriber flows pushed down.
--------------------------------------------------------------------
FlowDecomposer should work as-is or with minimal changes. Any changes could be made to help make the FlowDecomposer more agnostic to topology.

## Slide 13: Thank You

## Slide 14: Backup slides

## Slide 15
DPU
CPE
DPU Adapter
CPE Adapter
CPE Adapter
DPU Adapter
DPU HAL
CPE Adapter

## Slide 16: Interaction With L0/L1 Aspects
ONOS SDN Controller
VOLTHA
Three modeled use cases. VOLTHA should support all.
OLT
ONU / ONT
DPU
CPE / RG
OPENFLOW
RESTCONF / NETCONF
Kafka

## Slide 17: Interaction With L0/L1 Aspects
ONOS SDN Controller
Three modeled use cases. VOLTHA should support all.
  VOLTHA Device Adapter default configurations  Tie into service profile proposal
VOLTHA
OLT
ONU / ONT
DPU
CPE / RG
OPENFLOW
RESTCONF / NETCONF
Kafka

## Slide 18: Interaction With L0/L1 Aspects
ONOS SDN Controller
Three modeled use cases. VOLTHA should support all.
  VOLTHA Device Adapter default configurations  Tie into service profile proposal
  L0/L1 handled via ONOS apps and isolated  Tie into DCB? May now be undesirable?
NETCONF
VOLTHA
OLT
ONU / ONT
DPU
CPE / RG
OPENFLOW
RESTCONF / NETCONF
Kafka

## Slide 19: Interaction With L0/L1 Aspects
ONOS SDN Controller
Three modeled use cases. VOLTHA should support all.
  VOLTHA Device Adapter default configurations  Tie into service profile proposal
  L0/L1 handled via ONOS apps and isolated  Tie into DCB? May now be undesirable?
  L0/L1 handled by an orchestrator or other controller  OSAM? May now be undesirable?
ACCESS ORCH or CTRL
NETCONF / RESTCONF
VOLTHA
OLT
ONU / ONT
DPU
CPE / RG
RESTCONF / NETCONF
OPENFLOW
Kafka

## Slide 20: Discovery of DPUs Proposal
ONOS SDN Controller
VOLTHA
Alignment with other standards
  External Entity handle the Call homes and DHCP
  External Entity will subscribe to Kafka
  External Entity will use Restconf/Netconf to create/modify Devices Based on Network Plan
  VOLTHA rejoins Known Devices as it does today
  VOLTHA creates Kafka events for all Call Home events
  External Entity will trigger off this Call Home information
DPU
RESTCONF/NETCONF
OPENFLOW
Discovery / Call Home
NETCONF / RESTCONF
Kafka
Call Home Listener
Kafka